## Slide 1
St. Johns River Water Management District
Special Publication SJ97-SP8
Water Management Alternatives:
Effects on Lake Levels and Wetlands
in the Orange Creek Basin
G. B. “Sonny” Hall, Ph.D.
Bureau of Environmental Sciences

## Slide 2
The Problem
Man-made alterations within Orange Creek Basin (OCB) changed natural hydrology (flows and water levels)
Resulted in ecological degradation:
  Stabilization of water levels through construction of weirs
  Excessive growth of nuisance aquatic plants
  Water quality degradation
  Increased accumulation of sediments
  Declines in recreational fishing
2

## Slide 3
The Study
In response to these issues, SJRWMD completed a mid-1990s study to evaluate ecological value of alternative surface water management strategies
Study objectives:
Develop alternative water management strategies
Develop biohydrologic criteria to assess restoration and conservation potential of strategies
Identify which strategies require more specialized study (e.g., geologic, ecologic, or economic studies)
3

## Slide 4
Lake and wetland ecosystems require a range of surface water fluctuations for conservation
This range of water levels constitutes a fluctuation regime that consists of:
    High water levels due to temporary and seasonal floods
    Average (middle) water level
    Low water levels that coincide with mild droughts and infrequent extensive droughts
Water management options can increase or decrease range of lake water level fluctuations
4
Biohydrologic Criteria Development

## Slide 5
5
Five biohydrologic criteria were created to accommodate a range of surface water fluctuations
Criteria :
  Infrequent High
  Frequent High
  Middle
  Frequent Low
  Infrequent Low water levels
Criteria define hydrologic conditions required to preserve lake & floodplain wetland ecological processes
Biohydrologic Criteria Development

## Slide 6
6
Infrequent High Water Level
  A high water condition - occurs on average once every 5 years for a duration of 30 consecutive days (1:5 years, 30 days).
  Objectives:
  Inundate the entire floodplain wetlands - prevent encroachment of upland species
  Facilitate seed dispersal
  Transport organic matter between floodplain wetlands and lake
  To provide spawning, refugia, and foraging habitat for fish
Biohydrologic Criteria Development

## Slide 7
7
Frequent High Water Level
  A high water condition - occurs on average once every 2 years for a duration of 60 consecutive days (1:2 years, 60 days).
  Objectives:
  Maintain lower swamp and shallow marsh habitats
  Transport organic matter between floodplain wetlands and lake
  Provide spawning areas and refugia for small forage fish
  Provide foraging areas for other aquatic organisms, e.g., gamefish
  Facilitate seed dispersal
Biohydrologic Criteria Development

## Slide 8
8
Middle Water Level
Biohydrologic Criteria Development
  A low water condition - occurs on average once every 2 years for a duration of 180 consecutive days (1:2 years, 180 days).
  Objectives:
  Maintain wetland soils by preventing oxidation and subsidence
  Exclude colonization by terrestrial plants
  Maintain sufficient water depth in lake littoral zone for aquatic wildlife

## Slide 9
9
Frequent Low Water Level
  A low water condition - occurs on average once every 5 years for a duration of 180 consecutive days (1:5 years, 180 days).
  Objectives:
  Rejuvenate lake floodplain and littoral zone by allowing seed germination and growth of wetland plant species
  Increase rate of decomposition of organic sediments, allowing aerobic microbial breakdown
Biohydrologic Criteria Development

## Slide 10
10
Infrequent Low Water Level
  A low water condition - occurs on average once every 50 years for a duration of 360 consecutive days (1:50 years, 360 days).
  Objectives:
  Consolidate and compact organic sediments in fish spawning habitat
  Rejuvenate lake floodplain wetlands and upper littoral zone by allowing seed germination and growth
Biohydrologic Criteria Development

## Slide 11
11
Surface water levels generated by the SSARR model for water management alternatives plotted against the elevations of major plant community ecotones at Newnans Lake
Biohydrologic Criteria Development
wetter
wetter

## Slide 12
12
Other criteria were assessed:
Range of surface water fluctuation
Wetland extent
Change in boater access at 56 ft
Biohydrologic Criteria Development

## Slide 13
Twenty-three alternative surface water management strategies were evaluated
Ecological Evaluation of Water Management Scenarios
13

## Slide 14
14
Ecological Evaluation of Water Management Scenarios

## Slide 15
15
Ecological Evaluation of Water Management Scenarios

## Slide 16
Ecological Evaluation of Water Management Scenarios

## Slide 17
Ecological Evaluation of Water Management Scenarios

## Slide 18
Ecological Evaluation of Water Management Scenarios

## Slide 19
19
Ecological Evaluation of Water Management Scenarios

## Slide 20
20
Ecological Evaluation of Water Management Scenarios

## Slide 21
21
Ecological Evaluation of Water Management Scenarios

## Slide 22
Effects of different water management alternatives on the Orange Lake fluctuation regime (ft NGVD)
22
Ecological Evaluation of Water Management Scenarios

## Slide 23
23
Results of Biohydrologic Criteria Assessment at Orange Lake
Ecological Evaluation of Water Management Scenarios

## Slide 24
Surface water levels generated by the SSARR model for water management alternatives plotted against the elevations of major plant community ecotones at Orange Lake
24

## Slide 25
Assessed effects of management strategies on wetland extent
Utilized stage-duration and stage-area curves
25
Ecological Evaluation of Water Management Scenarios

## Slide 26
26
Ecological Evaluation of Water Management Scenarios
58.6
54.8
Extent of wetlands

## Slide 27
Ecological Evaluation of Water Management Scenarios
58.6
54.8

## Slide 28
Change in acreage for Orange and Lochloosa lakes wetlands for various water management alternatives
28
Ecological Evaluation of Water Management Scenarios

## Slide 29
Summary of wetland and hydrologic effects of surface water management alternatives for Orange and Lochloosa lakes
29
Ecological Evaluation of Water Management Scenarios

## Slide 30: Questions
30